## Slide 1: ELEMENTS OF COMPUTING
END SEMESTER PROJECT

## Slide 2: TEAM MEMBERS 01 03 02 04
G.SRI VATSANKA
CB.EN.U4AIE.21010
M.PRASANNA TEJA
CB.EN.U4AIE.21035
G.HIMAMSH
CB.EN.U4AIE.21014
VIKHYAT BANSAL
CB.EN.U4AIE.21076

## Slide 3: PART-1

## Slide 4: Conversion of files

## Slide 5: Required Steps:
Step-1
We will convert .Jack files to .VM files.
Step-2
Conversion of .VM files to .ASM files.
Step-3
.ASM files to hack files conversion.

## Slide 6: INTRODUCTION
We must develop a Jack code and use the Jack Compiler to compile the Jack file to VM file. Later, the VM file will be translated to an assembly language code file, which is abbreviated as ASM.
After developing the ASM file, that ASM file will be converted to a HACK file with help of ASSEMBLER.
The appropriate files, such as VM, ASM, and hack files, must be examined in the appropriate platforms, such as VM emulator, CPU emulator, hardware simulator. The NAND2TETRIS folder is the source of this program.

## Slide 7: JACK LANGUAGE
Jack is simple Object-based language that can be used to write High-Level programs .It has been a basic features and flavor of modern object-oriented language like java with much simpler syntax and no support for inheritance.
We use jack language as a means for teaching of,
Keyboard class allows the reading from a standard keyboard.
How to create a compiler.
To see how compiler and language interfere with the program.

## Slide 8: JACK Standard library
The jack programming language includes a standard library which can be seen as an interface to an underlying operating system. The Library is a set of jack classes that must be included in every jack implementation.
The following classes are included in a standard Library :
Math: Provides basic Mathematical operations.
String: Implements the string type & basic string-related operation
Array: Defines array type, array construction & disposal of array
Output: Handles text-based output.
Screen: Handles Graphic screen output.
Keyboard: Handles user input from the keyboard
Memory: Handles memory operations.
Sys: Provides some execution-related services.

## Slide 9: THE PROJECT
Returns the ASCII code (as char) of the currently pressed key, or 0 if no key is currently pressed.
Reads the next character from the keyboard: wait until a key is pressed and then released, then echos the key to the screen and returns the value of the pressed key.
Prints the message on the screen, reads the next line from the keyboard ,echoes the line to the screen, and returns it's value. This method handles user backspaces.
Prints the message on the screen, reads the next line from the keyboard ,echoes the line to the screen, and returns the integer until the first non-numeric character in the line. This method handles user backspaces.
Implementing Keyboard Library in Jack

## Slide 10: Keyboard Class
This class allows reading the input from the keyboard.
Function char keyPressed(): Returns the character of the currently pressed key on the keyboard ;if no key is currently pressed, returns 0.
Function char readChar(): waits until a key is pressed on the keyboard and released and echoes the key to the screen and returns the character of the pressed key.
Function string readLine(string message):Prints the message on the screen, reads the next line from the keyboard ,echoes the line to the screen, and returns it's value. This method handles user backspaces.
Function int readInt(string message):Prints the message on the screen, reads the next line from the keyboard ,echoes the line to the screen, and returns the integer until the first non-numeric character in the line. This method handles user backspaces.

## Slide 11: ASCII CODE
ASCII stands for "American standard code for information interchange".
ASCII is 7-bit character set containing 128 character.
It contains numbers from 0-9 ,the upper and lower cases English letter from A to Z and some special character(!,@,#,%,*...etc).
The characters are used in modern computers ,Html and on internet are based on ASCII code.

## Slide 12: ASCII TABLE

## Slide 13: Keyboard jack code

## Slide 14: Keyboard jack code

## Slide 15: Keyboard jack code

## Slide 16: Compiled Keyboard code

## Slide 17: Keyboard.vm code

## Slide 18: Main jack code

## Slide 22: Compiled MAIN code

## Slide 23: Main.vm code

## Slide 28: Main Test File
We have a test code in nand2tertris to crosscheck the keyboard library we created.
Location nand2tetrisprojects12keyboardtest.

## Slide 30
Keep all VM files in same folder.
To work with your own keyboard library, one can select and load the complete folder on VM Emulator.

## Slide 31: VM Implementation
Returns the ASCII code (as char) of the currently pressed key, or 0 if no key is currently pressed.
Reads their next character from the keyboard: wait until a key is pressed and then released, then echoes the key to the screen and returns the value of the pressed key.

## Slide 34: VM IMPLEMENTATION
Prints the message on the screen, reads the next line from the keyboard ,echoes the line to the screen, and returns it's value. This method handles user backspaces.

## Slide 36: VM IMPLEMENTATION
Prints the message on the screen, reads the next line from the keyboard ,echoes the line to the screen, and returns the integer until the first non-numeric character in the line. This method handles user backspaces.

## Slide 38: PART-2

## Slide 39: Topic
Write your own general purpose assembler to convert the assembly program into 16 bit machine codes also use the Nand2tetris assembler for conversion. (Your own assembler should be developed by you and is different from the assembler tool supplied along with the book)

## Slide 40: Assembler code

## Slide 44
Creating .hack for our keyboard library and Main file

## Slide 45
Comparing our KEYBOARD assembler file with the IN-BUILT assembler

## Slide 46
Comparing our MAIN assembler file with the IN-BUILT assembler

## Slide 47
Backup FILE!!

## Slide 48
Note: Firstly, one must convert .VM file to .asm file using a VM translator and then start working with assembler. We have to keep all the files in the same folder.

## Slide 49
Now in the terminal we use the command "python .\Assembler.py .\Max.asm" to convert asm.file to hack.file .

## Slide 50
Converting .asm file to .hack file using nand2tetris software, by using assembler tool.

## Slide 51
Both the hack files that we obtained using our own assembler and nand2teris are similar.

## Slide 52: PART-3

## Slide 53: Topic
Dump the machine codes generated by your own assembler into the Computer.hdl. Then design the architecture for implementing your machine instructions to get the result. (Here I presume that you already have the hdl scripts of all the hardware’s used by the CPU. Additional thing what you have to do is connecting the address and data buses during the execution).

## Slide 54: CENTRAL PROCESSING UNIT
The control unit is in charge of all CPU functions, including ALU operations, data transfer inside the CPU, and the interchange of data and control signals across external interfaces.
The control unit is in charge of all CPU functions, including ALU operations, data transfer inside the CPU, and the interchange of data and control signals across external interfaces.

## Slide 55: CPU Design
Instruction Memory -It contains a 16 bit ‘instruction’ as input and the output of PC can be explained based on Instruction memory.

## Slide 56: What does it mean by 16-bit Instructions?
There are two sorts of 16-bit instructions: A instructions and C instructions. Now, from the 0th to the 15th bit, if the first bit (i.e., the T-pin) is zero, it is an A instruction; if the first three bits are 1 1 1, or if the addition of the first bit is certain, it is a C instruction.
If the first bit is zero, the instruction is an A; if the first bit is one, the instruction is a C-instruction.
For the A instruction, the remaining 15 bits are value, which is saved in the A register and then outputs the value.
However, if I have a C instruction, then everything is entirely different. In this case, the 13 instruction bits are decoded into the Op-code (treat it as letter "a"), ALU control bits, Destination load bits, and Jump bits.

## Slide 57: Computer.hdl file

## Slide 58: Working with .hack file of KEYBOARD & MAIN

## Slide 59: Working with .hack file of KEYBOARD & MAIN

## Slide 60: Working with .hack file of KEYBOARD & MAIN

## Slide 61: ALTERNATE CODE[MAX ASM]

## Slide 62: ALTERNATE CODE[MAX HACK]

## Slide 63: CONCLUSION
In this project we have implemented and shown
How a Keyboard works
How a Hack Computer works
How high level language is abstracted at machine level.

## Slide 64: THANK YOU